## Slide 1
CV Assist: A Real-Time Visual Assistance System for the Visually Impaired
Empowering Independence Through Open-Vocabulary Detection, Monocular Depth, Hand Tracking & LLM-Vision
Developed by Group 1

## Slide 2
Webcam
Input
OWL-ViT
Detection
MiDaS
Depth Est.
MediaPipe
Hand Track
Guidance
Controller
LOGIC PROCESSING LAYER
TTS
Output
Real-time Audio Guidance
Microphone
Whisper ASR
Input
Speech-to-Text Recognition
DeepSeek LLM-Vision
Multimodal Error Correction
Complete Data Flow Architecture

## Slide 3
Search for Any Object by Name
Model: OWL-VIT V2
Utilizes the Open-Vocabulary Vision Transformer, a CLIP-based detector that accepts free-text queries instead of relying on predefined classes.
Key Capability
Open-vocabulary, zero-shot detection from natural language queries.

## Slide 4
Accurate Distance Sensing from a Single Consumer Camera
CORE TECHNOLOGY
MiDaS_small — a lightweight monocular depth estimation model optimized for real-time inference on standard hardware.
FUNCTION
Dynamically generates per-pixel relative depth maps from a single RGB stream, enabling precise distance estimation between the user's hand and the target object without additional sensors.
KEY ADVANTAGE
Eliminates the need for expensive stereo cameras or LiDAR — runs entirely on any standard consumer-grade webcam.

## Slide 5
High-Fidelity 3D Hand Landmarks Enable Precise Spatial Alignment
TECHNOLOGY
Google MediaPipe Hands tracks 21 3D hand landmarks in real time, providing robust skeletal tracking from a standard RGB feed.
HAND POSITION
The centroid of key landmarks (wrist + finger bases) is calculated as the definitive "hand location" for spatial offset computation.
GESTURE STATES
OPEN HAND:
Reaching / Ready to grasp.
CLOSED FIST:
Object grabbed; task complete.
SPATIAL ALIGNMENT
The X-Y offset between the hand centroid and the object center drives the directional audio instructions.
PRECISION
Sub-centimeter accuracy enables fine-grained, highly responsive guidance as the hand approaches the target.

## Slide 6
Spatial Guidance and Control Logic
Guidance Controller
Hysteresis-Based Guidance
Prevents oscillation when hand is near alignment boundaries by implementing directional hysteresis thresholds.
Example: Horizontal Alignment
Enter "left" zone:
x < -50px
Exit "left" zone:
x > -30px
Enter "right" zone:
x > 50px
Exit "right" zone:
x < 30px
20px deadband prevents rapid instruction switching
DYNAMIC FRAME SKIPPING
HIGH-FREQUENCY (30 HZ): HAND TRACKING (MediaPipe)
LOW-FREQUENCY (5 HZ): OBJECT DETECTION (OWL-ViT/MiDaS)
Intelligently skip LLM inference for object & depth when motion is low, maintaining high perceived smoothness on ordinary devices.
The GuidanceController is the system's decision-making core, transforming raw detection data into actionable spatial instructions.
Input:
Object bbox, depth value, hand landmarks
Process:
Spatial relationship calculation
Output:
Natural language instructions

## Slide 7
Voice Interaction: ASR and TTS
ASR: Automatic Speech Recognition
TTS: Text-to-Speech
High Light：LLM-Assisted Keyword Extraction
Engine:
OpenAI Whisper (local execution)
Language:
Chinese (zh)
English (en)
Activation: Press 'v' key to start voice input
Backend Options
pyttsx3
Offline
Basic quality, no setup required
MiMo (Xiaomi)
Cloud
High quality, requires API key
Whisper transcribes the command; DeepSeek-v3 uses both to return the most likely object name based on visual context.
The system uses LLM-Vision multimodal fusion to correct ASR errors in real time, achieving precise user intent alignment.

## Slide 8
Dual-Threshold Logic Delivers Stable, Professional-Grade Audio Instructions
THE PROBLEM: INSTRUCTION JITTER
Naive threshold-based guidance causes rapid oscillation ("Left… Right… Left…") when the hand is near the alignment boundary, making the system confusing.
THE SOLUTION: HYSTERESIS ALGORITHM
Implements two distinct thresholds for state transitions: Enter Threshold (Outer): A new directional instruction is triggered only when the offset exceeds a larger boundary. Exit Threshold (Inner): The instruction is cancelled only when the offset drops below a smaller boundary.
THE RESULT: STABLE GUIDANCE
Creates a stable "dead zone" around alignment. Instructions are issued decisively and cancelled cleanly, ensuring calm and confident spatial audio feedback.
1D Spatial Offset Axis demonstrating dual-threshold state transitions for jitter-free interaction.

## Slide 9
System Performance Metrics
Task-Level Metrics
session_id
Session identifier (UUID)
task_id
Incremental task ID
end_reason
Completion cause
target_visible_frames
Stable detection count
first_target_detected_ts
First detection timestamp
report_status
JSON report emitted
Frame Processing Pipeline
det1
Object detection (OWL-ViT)
hand1
Hand detection/tracking
d1
Depth estimation (MiDaS)
g1
Guidance calculation
proc1
Total algorithm processing
e2e1
End-to-end frame loop
Task Lifecycle Timing
s2act
Search-to-Activate
task_duration
Wall-clock time
sup1
Post-suppression processing
tts1
First TTS offset
confirm_window
Pre-activation duration
FPS & Latency Stats
fps_avg
Average processing FPS
e2e_avg
Average end-to-end FPS
p50
Processing time median
p95
95th percentile
jitter
Standard deviation
det_run
Detection execution rate
depth_run
Depth estimation rate
Resource Monitoring
cpu
Process CPU utilization
mem
Resident Set Size (RSS)
gpu
CUDA allocated memory
net↑
Network upload throughput
net↓
Network download throughput
Voice Metrics
poe
Poe vision parsing
asr_latency
Speech recognition time
record_time
Audio recording duration
first_tts_latency
First TTS response
cam_fail
Camera read failure count

## Slide 10
Empowering Independence Through
Intelligent Assistance
Computer Vision
Open-vocabulary detection with zero-shot capability
AI Integration
LLM-enhanced voice recognition with visual context
Human-Centered
Designed for real users with real accessibility needs
Future work will expand gesture vocabulary and optimize deployment for edge devices. By integrating haptic feedback, we aim to evolve the system into a multi-sensory ecosystem for more intuitive human-spatial interaction.